## Slide 1
IMPLEMENTATION OF INTERNAL XADC BASED ADC AND SPI SERIAL TRANSMISSION ON ZYNQ-7000 FPGA
IIT (ISM) DHANBAD
MEMBER 1: Penmatsa Rethika Surya Sri
MEMBER 2: Menda Srihari Naidu
Under the supervision of
Prof.Rahul Bhattacharya

## Slide 2
Introduction
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
2/22
Real-world signals are analog, while FPGAs work with digital data — so an ADC is needed to convert analog signals into digital form.
The Zynq-7000 FPGA has a built-in XADC, which avoids the need for an external ADC and simplifies the hardware.
In this project, the internal XADC is used to sample the analog signal and produce corresponding 16-bit digital values.
These digital values are then transmitted using a custom SPI communication system designed and implemented in Verilog.
The work focuses on understanding timing concepts and verifying the design using the Integrated Logic Analyzer (ILA) for debugging

## Slide 3
Project overview
Use internal XADC in Zynq-7000 FPGA
Convert analog signal to 16-bit digital output
Transmit digital data using Verilog-based SPI interface
Debug internal signals using Integrated Logic Analyzer (ILA)
Focus on deep understanding of timing concepts
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
3/22

## Slide 4
Motivation
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Why Internal XADC?
Eliminates external ADC hardware
Reduces system complexity and cost
Faster access to sampled data
Compact, integrated design
Suitable for real-time FPGA applications
4/22

## Slide 5
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
XADC Basics
Built-in ADC inside Zynq-7000
Supports internal and external analog channels
Generates 16-bit digital output
VAUXP0/VAUXN0 connected to sine wave generator
Understanding Internal XADC
5/22

## Slide 6
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
System Clock vs ADC Clock
System Clock = 125 MHz (8 ns period)
XADC cannot run above 26 MHz
Internal clock divider generates 25 MHz
ADC Clock period = 40 ns
6/22

## Slide 7
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Acquisition vs Conversion Time
Wrong assumption corrected:
Acquisition time does NOT control sampling rate
Acquisition = charging time of sampling capacitor
4 cycles = 4 × 40 ns = 160 ns
Conversion rate actually controls sample output
7/22

## Slide 8
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Conversion Rate
DRDY goes high every 1040 ns
New data sample available each cycle
961.5 ksps
Tconv ≈ 1.04 µs
8/22

## Slide 9
SPI Protocol : Theory
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
SPI Basics
Synchronous serial communication
Used with sensors, DACs, memories, ADCs
Full duplex
Master controls clock and communication
9/22

## Slide 10
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
SPI Signals
SCLK – Clock from master
MOSI – Master → Slave
MISO – Slave → Master
CS/SS – Chip Select (Active Low)
10/22

## Slide 11
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Shift Register Operation
Master and Slave both use shift registers
On each clock edge:
• Bit shifts out from MOSI
• Bit shifts in from MISO
Works like circular buffer
11/22

## Slide 12
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
SPI Modes
Defined by CPOL and CPHA
Select edge for sampling and shifting
Ensures device compatibility
12/22

## Slide 13
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Advantages
Very high speed
Low power
Simple hardware
Full duplex
Flexible timing
13/22

## Slide 14
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Limitations
Requires 4 wires minimum
No addressing
No multi-master
More slaves require more GPIO
14/22

## Slide 15
SPI Implementation with XADC Data
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
SPI Clock Derivation
= 1040ns
1040/16 = 65 ns per bit
≈ 15.38 MHz
System clock = 8 ns
Count 8 cycles → 64 ns
Occasionally insert extra cycle
15/22

## Slide 16
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Master Module Operation
DRDY triggers transmission
CS becomes LOW
SCLK generated
16-bit shift transmission happens
16/22

## Slide 17
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
SPI Slave Behaviour
16-bit register stores XADC data
On each falling edge:
• MSB sent to MISO
• Register shifts left
• Reloads after 16 bits
17/22

## Slide 18
Integrated Logic Analyzer
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
ILA Debugging
10kHz → 100000ns
100000 / 8 = 12500 samples
Depth set to 32k
Observed:
• XADC output
• DRDY
• SPI Clock
• Chip select
• MISO data
18/22

## Slide 19
Results
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
XADC produced clean sampled waveform
SPI serialized data correctly
Timing matched theory
Debugging verified correct design
19/22

## Slide 20
Generation Of Sine Wave Using Ram

## Slide 21
Simulation Results Of SPI Protocol

## Slide 22
XADC Output

## Slide 23
XADC Output on ILA

## Slide 24
Experimental Setup and Connections

## Slide 25
Interfacing PMOD AD5 with Zynq-7000 FPGA
Communication protocol: SPI
Purpose: High-resolution differential voltage measurement
FPGA controls ADC and reads digital output
Data observed using Integrated Logic Analyzer (ILA)

## Slide 26
PMOD AD5 Key Features
24-bit resolution ADC
4 differential / 8 pseudo-differential inputs
SPI interface (MSB first)
On-board 2.5 V reference
50/60 Hz noise rejectionDefault gain = 128
default conversion time ≈ 100 ms

## Slide 27
SPI Communication Sequence
Step 1: CS → LOW (start communication)
Step 2: Wait 100 ms (conversion & settling time)
Step 3: Send 0x58 (Read Data Register command)
Step 4: Read 24-bit ADC data via MISO
Step 5: CS → HIGH (end communication)

## Slide 28
Verilog FSM Implementation
SPI controlled using Finite State Machine (FSM)
States:
S0: Idle (CS high)
S1: CS low
S2: 100 ms delay
S3: Send command (0x58)
S4: Read 24-bit ADC data
S5: CS high, restart
SCLK generated using clock divider
Shift register used for serial data reception

## Slide 29
Output and Debugging
ADC data stored in 24-bit register (adc_out)
MISO, MOSI, CS, SCLK monitored using ILA
Verifies:
Correct SPI timing
Command transmission
Data reception accuracy
System ready for further processing in FPGA/PS

## Slide 30
Output Waveform Observed on ILA

## Slide 31
Conclusion
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Internal XADC successfully replaces external ADC
Custom SPI designed and verified
Strong learning on timing and FPGA debugging
20/22

## Slide 32
Future scope
Implementation of Internal XADC Based ADC and SPI Serial Transmission on Zynq-7000 FPGA
Interface with external microcontroller
Add DAC to reconstruct signal
Implement digital filters
Real-time display GUI
Future work
21/22

## Slide 33
Thank you for listening!
For more information contact :
Penmatsa Rethika Surya Sri
Menda Srihari Naidu